## Slide 1: Lab# Digital Modulation

## Slide 2: ASK (Amplitude Shift Keying)
2 กลุ่ม ผลัดกันส่งและรับข้อมูล
Tx: PC -> Arduino -> DAC -> ASK signal
Rx: ASK signal -> Arduino -> PC

## Slide 3: ASK (Amplitude Shift Keying)
ASK Signal
  Sinewave ขึ้นกับข้อมูล 2 บิตที่อ่านเข้ามา
  Sinewave sample ที่มุม 0, 90, 180, 270 จะใช้เวลาส่งห่างกันเท่าไหร่ ขึ้นกับความถี่ของ sinewave ที่ต้องการสร้าง
    เช่น f0 = 500Hz
    T = (1/f0) = (1/500) = 2 ms = 2000 us = 10^6/500 us = 1,000,000 / f0
    1 T (คาบ) แบ่งส่ง 4 ค่า sine ที่มุม 0, 90, 180, 270
      ดังนั้นระยะเวลาส่ง ระหว่างมุม T/4

## Slide 4: ASK (Amplitude Shift Keying)
Theory
  Sending each sin(zeta) should takes only T/4
Practical
  DAC has a limited transmission speed (default_freq = 1700 Hz)
  This causes a delay time inside DAC for each sine(zeta)
    delayDAC = (1/default_freq)/4
  Total delay between sine sample (sin(zeta))
Delay_sample_theory =
Delay_sample _practical
=
delay0 =

## Slide 5: ASK (Amplitude Shift Keying)
delay0 =
Read all inputs
Sine property selection
Get 2 bits at a time -> select Amplitude A
send A* sin[i]
delay0
AnalogRead
Amplitude decision
Decode 2 bits
Send data
1 baud = sine 5 cycle

## Slide 6: ASK (Amplitude Shift Keying)
กำหนดให้
% A คือ ASK Amplitude ที่เลือก
A=[A1, A2, A3, A4]
% อยู่ในช่วงของไฟ arduino คือ 0<= A <= 5
% S เป็นค่า sine 4 samples ที่ตำแหน่งมุมต่างๆ
S = [Sin(0), Sin(90), Sin(180), Sin(270]
% ค่า sine นี้ สำหรับ DAC 12 bits [0, 4095]
% มาจากการทดลองที่ 6.3

## Slide 7: ASK (Amplitude Shift Keying) Modulation
Read All Digital inputs N Bytes
x[i]
Get 2 bits of x[i]
Select A[j], n cycles
Send A[j]*sine[k]
delay0
For k = 1:4
end
For 2bitSet[j] = 1:4
end
For input byte i = 1:N
end
For p = 1:n
end

## Slide 8: ASK (Amplitude Shift Keying) Demodulation
1) Read sample input from AnalogRead()
2) Define Max Amplitude of Sine sample
3) From Max Amplitude
-> decode 2 bits
4) Collect all 8 bits (4 x 2bits)
5) Store 8 bits in an array
6) All data bytes
Yes -> Done
No -> Repeat 1-6

## Slide 9: FSK (Frequency Shift Keying)
delay =
Read all inputs
Sine property selection
Get 2 bits at a time -> select frequency f
send sin[i]
Delay ตาม f
วนส่ง N cycles (รอบ)
AnalogRead
Amplitude decision
Decode 2 bits
Send data
baud = 250 Hz (Signal_units/s)
-> Tbase = 400 us
f = 500 -> delay0 -> N = 2 cycle
f = 750 -> delay1 -> N = 3 cycle
f = 1000 -> delay2 -> N = 4 cycle
f = 1250 -> delay3 -> N = 5 cycle

## Slide 10: FSK (Frequence Shift Keying)
Read All Digital inputs N Bytes
x[i]
Get 2 bits of x[i]
Select delay(f), n (cycles)
Send sine[k]
delay(f)
For k = 1:4
end
For 2bitSet[j] = 1:4
end
For input byte i = 1:N
end
For p = 1:n
end
f1, n1
f2, n2
f3, n3
f4, n4
baud = 250 Hz (Signal_units/s)
-> Tbase = 400 us
f = 500 -> delay0 -> N = 2 cycle
f = 750 -> delay1 -> N = 3 cycle
f = 1000 -> delay2 -> N = 4 cycle
f = 1250 -> delay3 -> N = 5 cycle

## Slide 11: FSK (Frequence Shift Keying)
f1, n1
f2, n2
f3, n3
f4, n4
baud = 250 Hz (Signal_units/s)
-> Tbase = 400 us
f = 500 -> delay0 -> N = 2 cycle
f = 750 -> delay1 -> N = 3 cycle
f = 1000 -> delay2 -> N = 4 cycle
f = 1250 -> delay3 -> N = 5 cycle
1) Read sample input from AnalogRead()
2) Define Sine period (T)
3) From T, calculate f
-> decode 2 bits
4) Collect all 8 bits (4 x 2bits)
5) Store 8 bits in an array
6) All data bytes
Yes -> Done
No -> Repeat 1-6

## Slide 12: FSK (Frequency Shift Keying) Demodulation
1) Read sample input from AnalogRead()
2) Define Sine period (T)
3) From T, calculate f
-> decode 2 bits
4) Collect all 8 bits (4 x 2bits)
5) Store 8 bits in an array
6) All data bytes
Yes -> Done
No -> Repeat 1-6